# GRADES AVAILABLE – LANCER BRAKE OIL

#### CHARACTERISTICS

| GRADE | Lancer Brake Oil |
| --- | --- |
| Kin. Viscosity @ (-)40ºC, cSt, Max 100ºC cSt, Min | 1300 2.0 |
| Equilibrium Reflex Boiling Point, ºC, Min | 255 |
| pH Value | 8.5 – 10.5 |

# Text boxes

# PERFORMANCE STANDARDS

- SAE J 1703 for Hydraulic Brake Fluid, Heavy Duty

- FM VSS No. 116 DOT 4.

# APPROVAL

## Lancer Brake Oil is approved for Mitsubishi Lancer cars.

# PERFORMANCE BENEFITS

- Prevents vapour lock problems in high temperature operating conditions.

- Has improved low temperature characteristics and can be safely used in cold climate.

- Provides excellent protection against corrosion to iron, non-ferrous metals and zinc alloys.

- Ensures long service life of Brake Fluid and components of brake mechanism.

# APPLICATION

Lancer Brake Oil is recommended for hydraulic brake systems including disc type fitted in Mitsubishi Lancer vehicles.

### DESCRIPTION

Lancer Brake Oil is a heavy duty hydraulic brake fluid processed from carefully selected ingredients and incorporates a balanced combination of anti-oxidants, metal deactivator and corrosion inhibitor.