# GRADES AVAILABLE – SERVO CKD (SKODA) GENUINE DG SET OIL

# CHARACTERISTICS

| SAE GRADE | 40 |
| --- | --- |
| Kin. Viscosity @ 100(C, cSt | 13-15 |
| Viscosity Index, Min | 90 |
| Flash Point (COC), (C, Min | 225 |
| Pour Point, (C, Max | (-) 6 |

# Text boxes

# PERFORMANCE BENEFITS

- Effectively combats the deleterious products of combustion associated with high sulphur fuels, thus minimising deposits and wear.

- Maintains excellent engine cleanliness by holding contaminants in finely dispersed suspension thus reducing formation of lacquer, varnish and sludge.

- Minimise deposits resulting from high output, low speed, and low temperature operations.

- Provides excellent control of cold sludge and corrosive wear.

# PERFORMANCE STANDARDS

Meets the following specifications –

- API Service CD

- Caterpillar Series 3

- Ford M2C-87/88

- IS:EDL 2 of BIS 13656-1993

- US Military MIL-L- 45199B

# Manufacturers Approval

M/s. CKD HRADEC KRAOVE A.S. Czech republic the manufacturers of CKD (SKODA) Diesel Generating Sets has approved the use of Servo CKD (SKODA) Genuine DG Set Oil for all CKD (SKODA) Diesel Engines and Diesel Generating Sets.

# APPLICATION

Servo CKD (SKODA) Genuine DG Set Oil is recommended for all CKD (SKODA) Diesel Engines and Diesel Generating Sets manufactured by M/s. CKD HRADEC KRALOVE A.S. Czech Republic and operating on distillate fuel.

DESCRIPTION

Servo CKD (SKODA) Genuine DG Set Oil is state of the art technology.  Product manufactured from high viscosity index base stocks and contains appropriate dosages of detergent-dispersant and antioxidant additives to meet the International Performance Standards.   The product has demonstrated capability to ensure trouble free and extended engine life coupled with longer oil drain periods.