GRADES AVAILABLE - -SERVO XEE SL  5W-20, 10W-40

# CHARACTERISTICS

| SAE GRADE | 5W-20 | 10W-40 |
| --- | --- | --- |
| Kin. Viscosity @ 100ºC, cSt | 8.0 – 9.3 | 13.5 – 15.5 |
| Viscosity Index, Min | 145 | 135 |
| Flash Point, COC, ºC, Min | 190 | 200 |
| TBN, mg KOH/gm | 7.0 | 7.0 |

# Text boxes

# PERFORMANCE BENEFITS

- Superior wear protection.

- Superior deposit control.

- Extended component life.

- Excellent engine cleanliness.

- Lower oil consumption

- Better Fuel Economy

- Catalytic Convertor Compatible.

# PERFORMANCE STANDARDS

- API SL in gasoline service.

- Comply with ILSAC GF-3 Performance.

# APPLICATION

Servo XEE SL oils are recommended for new generation imported and Indian passenger cars using petrol.

DESCRIPTION

Servo XEE SL oils are premium long life, high performance fuel economy engine oil for new generation petrol vehicles.   These oils are blended from high viscosity index base stocks and contain additives to meet the highest quality performance standard.