# GRADES AVAILABLE - SERVOKOOL ALT

CHARACTERISTICS

| Appearance | Blue clear liquid |
| --- | --- |
| Specific Gravity @ 20°C, Min. | 1.114 |
| Boiling Point, ºC, Min | 155 |
| Freezing Point, ºC 30% Volume Solution 50% Volume Solution | (-) 14 (-) 34 |
| pH of 30 v/v % Soln in distilled water | 7.5 – 9.0 |

# Text boxes

### DESCRIPTION

Servokool ALT is a triple action long life radiator coolant prepared from selected ingredients to meet the highest Japanese standard and is free from Amines, Borates, Nitrates and Silicates and Phosphates.

# APPLICATION

Servokool ALT is recommended for passenger cars, light commercial vehicles, heavy vehicles and heavy earth moving equipment as a radiator coolant.     For desired performance 30 parts of the fluid is to be diluted with 70 parts of distilled water in most of the vehicles.

# PERFORMANCE BENEFITS

- Does not boil and vaporise in the hottest summer or freeze in severe  winter.

- Prevents corrosion of radiator components and other parts.

- Increases cooling efficiency.

- Reduces maintenance costs and increases radiator life.

# PERFORMANCE STANDARDS

- JIS K 2234-1994  CLASS 2