## Slide 1: Net Zero Emissions Target
25th August 2022

## Slide 2: India’s climate commitment at COP26, Glasgow (Panchamrit)
1
Enhance non-fossil fuel energy capacity to 500 GW by 2030
2
Meet 50% of energy requirements from renewable energy by 2030
4
Reduce carbon intensity of economy by less than 45% by 2030 (base year 2005)
3
Reduce projected carbon emissions by 1 billion tonnes from now onwards till 2030
5
Achieve Net Zero emissions by 2070
Hon’ble PM Shri Narendra Modi at the COP 26 Meet in Glasgow
Notes:   Installed capacity – 396 GW (Thermal – 236 GW / RE – 106 / Hydro – 46 / Nuclear – 7)
  India Emission 2020: 2.7 Billion tons of CO2e (Energy emission – 2.3 billion tons)
GHG Gases - Carbon dioxide (CO2), Methane (CH4), Nitrous oxide (N2O), Hydrofluorocarbons (HFCs), Perfluorocarbons (PFCs), Sulfur hexafluoride (SF6), Nitrogen trifluoride (NF3)

## Slide 3: Emissions being targeted for Net Zero
Scope-1 Emissions
GHG emissions from assets and activities that fall within organizational boundary.
Scope-2 Emissions
GHG emissions on account of purchased electricity consumed in operations.

## Slide 4: GHG Emissions (Scope-1 & 2) Standalone Performance in FY 2021-22
Parameter | Unit | Operations |  | 
 |  | Refinery + Petrochemicals | Pipeline Transport | Product Storage / Blending
Scope-1 Emission | MMTCO2e | 20.67 | 0.10 | 0.05
Scope-2 Emission | MMTCO2e | 0.24 | 0.27 | 0.21
Operational Emission (Total) | MMTCO2e | 20.91 | 0.37 | 0.26
IndianOil Emission (Standalone) | MMTCO2e | 21.54 |  | 
% Contribution to Emissions | % | 97% | 2% | 1%
Emission incl. CPCL, Chennai | MMTCO2e | 24.40 |  | 

## Slide 5: GHG Emission Projection Annual Numbers
Refinery & Petrochemicals*
23.53 MMTCO2e
Scope-1 Emission
0.24 MMTCO2e
Scope-2 Emission
24.40 MMTCO2e
Total Emission
0.63 MMTCO2e
Marketing, Pipelines, R&D and BD: Scope 1&2
Other Divisions
10.75 MMTCO2e
Scope-1 Emission
5.09 MMTCO2e
Scope-2 Emission
16.04 MMTCO2e
Total Emission
0.20 MMTCO2e
Marketing, Pipelines, R&D and BD: Scope 1 + 2
34.28 MMTCO2e
Scope-1 Emission
5.33 MMTCO2e
Scope-2 Emission
40.44 MMTCO2e
Total Emission
0.83 MMTCO2e
Marketing, Pipelines, R&D and BD: Scope 1+2
>97%
Current Emissions
(A)
Emission from Expansion
Projects (B)
Total Emission
(C) = (A) + (B)
* Data includes CPCL Emission

## Slide 6: Emission Mitigation (FY 2021-22)
S. No. | Initiative | Emission Mitigation / Avoidance (MMTCO2e)
1. | Use of Natural Gas instead of Liquid Fuels | 1.60
2. | Pipelines Transportation of crude / fuels (75% emission reduction as compared to rail) | 1.13
3. | Renewable Energy of ~240 MW (Solar: ~70 MW; Wind: ~170 MW) | 0.28
4. | Energy Conservation Projects in refineries Savings of 67,000 SRFT | 0.22
5. | Emission Offset Estimated ~40 lakh surviving plantations within & beyond boundary | 0.08
6. | LEDs installed across the company (~8 lakh nos.) | 0.05
TOTAL |  | 3.36

## Slide 7: Commitments towards NET ZERO Reducing Operational Emissions
Mitigate Scope-1 & 2 emissions across our wholly owned domestic assets, on an absolute basis, by the year 2046.
Wheels in Motion…
CCUS
1500 TPD EOR Project with ONGC
Green Hydrogen
5 KTPA & 2 KTPA units being installed at Refineries
Natural Gas
Increasing adoption of Natural Gas in refineries in place of liquid fuels
Energy Efficiency
Energy audits / efficiency projects are undertaken to reduce emissions
In pursuit of this ambition, we are undertaking measures such as energy efficiency, low carbon fuel switch, renewable energy, shift to grid power, nature-based solutions and CCUS.

## Slide 8: Commitments towards NET ZERO Reducing Operational Emissions
Meeting the electricity requirements of expansion projects in refineries through renewable sources
Grid & RE Power
Anticipating lower grid emissions, the company is encouraging Grid & RE Power for existing plants including Refineries
Wheels in Motion…
RE Power for Expansion Projects
Collaboration with NTPC to source ~2.3 GW RE to meet power requirement of refinery expansion projects

## Slide 9: Commitments towards NET ZERO Creating an enabling environment to support actions beyond boundary
  Increase the proportion of greener fuels in the product mix being offered to consumers
Wheels in Motion…
  Ethanol blending crossed 10%
  100 KLPD 2G Ethanol project at Panipat
  128 KLPD 3G Ethanol plant at Panipat (U/C)
  CBG Plants at Hingonia (6 TPD) & Gorakhpur (25 TPD, U/C)
  Waste Plastic to Fuel developed (INDEcoP2F)
  2000+ EV Charging Stations (Target: 10,000/ 3 yrs)
U/C: Under Construction

## Slide 10: Commitments towards NET ZERO Creating an enabling environment to support actions beyond boundary
  Invest in low carbon energy technology and undertake partnerships to improve product efficiency
    Rs. 577 Cr R&D expenditure (RE, Bio-energy, Fuel Cell, Greener Products etc)
    Pursuing partnerships with NTPC, L&T, RE Power
  Engage with value chain partners to reduce emissions across current network
    Energy Efficiency / Automation / Solarisation (~20,000 nos.) in Retail Network
    Phasing-out old fleet from fuel transport, switching to pipelines & inland shipping from rail / road
  Bring greater linkages between employee performance & company climate targets
  Establish IndianOil as a leader in environment sustainability, providing support to the nation & fellow corporates in reducing environment & climate impact

## Slide 11: Net Zero Approach Activity Timelines
  Complete GHG inventory
  Validation & Monitoring of Mitigation Targets vis-a-vis Plans
  ENCON Schemes
  Renewable Energy
Short Term
(1-2 Years)
  ENCON Schemes
  Switch to NG
  Grid electricity
  Tree Plantation
  CCUS
  Renewable Energy
Medium Term
(2-5 Years)
  Boiler / Furnace Efficiency
  Grey to green hydrogen (25%)
  Grid electricity
  CBG
  Green Hydrogen
  Tree Plantation
  CCUS
  Renewable Energy
Long Term
(5-10 Years)
  Improving Boiler / Furnace efficiency
  Grey to green hydrogen (100%)
  Maximizing grid import
  Improve Distillate Yield
  CBG
  Green Hydrogen
  Tree Plantation
  CCUS
  Renewable Energy
Natural (>10 Years) Investment Cycle

## Slide 12: Envisaged Emission Mitigation Pathway

## Slide 13: Limitation / Boundary for Net Zero
Boundary* | The target is set for 100% of operational emissions from IndianOil business units, namely refineries, petrochemicals, pipeline transportation and storage / distribution terminals and plants, located within the geographical boundary of India. Refineries of our subsidiary, Chennai petroleum Corporation Limited (CPCL) have been included within the ambit of these net zero commitments. GHGs covered: CO2, CH4 and N2O Scope-3 emissions (such as end use of products, emission from product distribution and retail network) are also excluded from current net zero boundary.
* Emissions currently exclude BOO projects, retail network, JV Companies and overseas operations

## Slide 14
ACHIEVE NET ZERO OPERATIONAL EMISSIONS
2046

## Slide 15
Thank You